## Slide 1: Summary | Oceans & Hydrology - Inland Water & Coastal Sea Level
Lake & Reservoir Volume in S. America – MODIS and ICESat-2, RA from DAHITI for cross-validation (Carabajal and Boy)
  Take-home: use the altimetry simultaneously invert for the time-variable water elevation (constant in space) and the space-variable geoid (constant in time)
Improving tide models of polar ocean, w/ multi-mission data including CryoSat-2 (Hart and Davis et al.)
  Take-home: releasing new EOT-Polar tide model in 2025. Full-estimation tide model that includes new gridding strategy and CryoSat-2 orbit and pseudo-repeat
High-latitude lake and river dynamics (Birkett)
  Take-home: looking for elevation slope and depth (Alaska), applied sciences project with multiple US agencies. Plea for ICESat-2 ATL13: tool/app that IDs ATL13 polygon number quickly
Large Lake Ice Classification / Freeboard (Peter and Anderson)
  Take-home: large lakes require Sea-Ice-like ATL products but redeveloped for large lakes. GMASI ice/water classification is no good for large lake classification (67% accurate) -> new method is ~94%
Coastal Mean Sea Level (Buzzanga and Hamlington)
  Take-home: ICESat-2 ATL12 complements reference radar altimetry and improves comparison with tide gauges
Sea State Bias and SSH in Estuaries (Putnam et al.)
  Take-home: Radar altimetry footprints are too big, ICESat-2 much finer resolution -> can get into estuaries. IS2 can improve/explain bias in radar altimeters. Recommend using ATL13 (instead of ATL12) -> good for narrow estuaries and fjords

## Slide 2: Summary | Oceans & Hydrology - Oceans
Variability of the Antarctic Coastal Current using ICESat-2 and CryoSat-2 altimetry (Sahra Kacimi et al)
  Take-home: IS2 used for new DOT and Antarctic Circumpolar Current with comparison to radar altimetry estimates. Regional specific processing (geoid, etc) needed near the coasts.
Update on CryoSat’s Long-Term Ocean Data Analysis and Validation (Marc Naeije et al)
  Take-home: Performance of CS2 ocean products (baseline C) assessed. Evolution to baseline D shows adjustments and overall performance is good and passed quality control.
ICESat-2 Ocean Altimetry (Alexa Putnam et al)
  Take-home: IS2 ocean DOT products ATL12 and ATL23 assessed in detail and compared to equivalent CS2 DOT products. SSB differences call for improved radar SSB calculations.
Inferring subsurface density changes in ice-covered oceans from ICESat-2 and GRACE Follow-On observations (Rui Ponte)
  Take-home: IS2 and AVISO (radar) DOT products compared to each other and against ECCO model. Consistent results in the Arctic but larger differences in Antarctic. Altimetry can help constrain models.