## Slide 1
Seed Questions
Session 4: Wind & Waves
Chairs: Sonia Ponce de León and Lotfi Aouf

## Slide 2
Seed questions discussion
What sampling (1 Hz, 5 Hz, 20 Hz) of SWH from altimetry is skilled for the assimilation in coastal wave models? Skillfulness to small-scale variability induced for instance by wave/currents interactions? Sub-kilometric HR altimeter data is required to improve coastal analysis of altimeter data.
Relevance of accurate estimate of SWH and wave period (Wang et al. 2021) from altimetry to improve accounting sea state bias (SSB) in the algorithms of sea level retrieval in coastal areas?
Are we able to correctly estimate extreme wave height events in the coastal zone with satellite altimetry?
What use of improved SWH estimate (CCI, F4 alti,…) for future development of high-resolution wave reanalysis for example 1/36° grid size for CMEMS-IBI in 2023? availability of 5 Hz?
Extending the use of directional wave spectra from Sentinel-1 and CFOSAT missions in coastal areas? Retrieval of wave spectra from S1 images and future missions Harmony and SEASTAR (proposed for EE11)?
Coastal wave buoys are key to assessing altimeter performance in the coastal zone, yet the altimeter-buoy collocation methods should be adapted to account for enhanced sea state variability. Drifting wave buoys are now available and could be useful for CAL/VAL studies.

## Slide 3
Can we expect directional wave spectra from fully focused SAR processing in altimetry dedicated to coastal applications?
FFSAR can solve the missing variable wave period from altimetry.
Directional variability is relevant for forcing models dedicated to wave overtopping and flooding near shore prediction and also to better analyze wave projections in climate scenarios (accounting of wave set(-up)?
How about the use of high-resolution SAR winds from Sentinel-1 to better forecast sea state in coastal areas?
Sea State CCI has reprocessed along-track altimetry with strong benefits for coastal observations. Gridded products nevertheless are still produced as averaged boxes with a 1°x1° resolution without any coastal consideration. Is there an interest to fill the gaps among the tracks with refined spatio-temporal interpolation or are along-track data considered more useful for coastal analysis despite the gaps?
Seed questions discussion

## Slide 4
Recommendations
We recommend to ESA launch more calls on waves to perform research!
We ask ESA to support the development of this research activity (develop new retrackers and processing with the SAMOSA+ missions such as CryoSat-2), and support the retrieval of SWH, SL.
We recommend to ESA and other space agencies support the creation of coastal altimetry products to fill the gaps in the coastal zone with the highest possible spatial resolution (approx. 150 meters).
To the in-situ data agencies such as Puertos del Estado and CMEMS, we recommend installing more wave buoys to monitor the African coasts in the Mediterranean Sea where the assessment of wave power is needed urgently, and elsewhere, e.g., near the Atlantic African coast. The number of coastal wave buoys needs to be increased to assess the quality of the coastal altimetry products.
Real-time coastal altimetry products are needed for the operational wave forecast.

## Slide 5
Recommendations
Global coastal high-resolution wave modelling is a prerequisite to foster the evaluation and exploitation of coastal altimetry SWH data at global scale. High-resolution (~200m) wave models with accurate coastal atmospheric are necessary to optimize the synergistic use of altimeter and in situ wave data.
The availability of coastal drifting wave buoys for the gridded products we need a better sampling that fits the use in the validation or assimilation in the wave forecast.
SARwave and the availability from wave spectra in the coastal zone.
Reprocessing historical directional missions such as Envisat for the implementation of wave reanalysis.